## Slide 1
SOAR
(smart linker)
MicroEJ Application executable file
Font Generator
Image Generator
Font
Designer
*.class
*.class
font
*.ejf
*.class
*.class
font
*.ejf
*.class
*.class
font
*.ttf
*.class
*.class
image
*.png
*.class
*.class
Java class files
*.jar
*.class
*.class
Java class file
*.class
*.class
*.class
resource
*.*
*.class
*.class
image
*.jpg
*.class
*.class
image
*.png
*.class
*.class
image
*.bmp
MicroEJ platform
(runtime)
UI engines (C modules)
Display / Input / LED

## Slide 2: Introduction
Display continuous refresh
Memory
Width * Height * BPP / 8
Drawings
Notes: Stéphane
The LCD continuously refreshes its content by reading the data from a memory buffer.
  The buffer size depends on the LCD size and its number of bits per pixel.
  We cannot stop this refresh, otherwise the image fades away.
A new frame often appears every 16.6ms (60Hz).
The electric signals may be generated by an internal LCD controller in the LCD device or by a LCD controller in the MCU.
The electric signals frequency is several MHz
If we draw at the same time and in the same buffer than the LCD, we will see the drawings “one by one” instead of seeing the entire frame at once

## Slide 3: Introduction
MCU
Display module
Display continuous refresh
Memory
LCDC
SPI
Memory
Notes: Stéphane
The LCD continuously refreshes its content by reading the data from a memory buffer.
  The buffer size depends on the LCD size and its number of bits per pixel.
  We cannot stop this refresh, otherwise the image fades away.
A new frame often appears every 16.6ms (60Hz).
The electric signals may be generated by an internal LCD controller in the LCD device or by a LCD controller in the MCU.
The electric signals frequency is several MHz
If we draw at the same time and in the same buffer than the LCD, we will see the drawings “one by one” instead of seeing the entire frame at once

## Slide 4: Introduction
MCU
Display module
Display continuous refresh
LCDC
LCDC
Memory
Notes: Stéphane
The LCD continuously refreshes its content by reading the data from a memory buffer.
  The buffer size depends on the LCD size and its number of bits per pixel.
  We cannot stop this refresh, otherwise the image fades away.
A new frame often appears every 16.6ms (60Hz).
The electric signals may be generated by an internal LCD controller in the LCD device or by a LCD controller in the MCU.
The electric signals frequency is several MHz
If we draw at the same time and in the same buffer than the LCD, we will see the drawings “one by one” instead of seeing the entire frame at once