## Slide 1: Overview (Custom)
Kernel.install(InputStream)
.fo
1
Transfer bytes stream
Code to temporary location
Resources to target location
2
Transfer code to target location
3
4
Free temporary locations
Apply code relocations
Feature.start()

## Slide 2: MemorIES (Custom)
Kernel Working Buffer
(TEMPORARY code)
RAM
ROM
Java Heap
(TEMPORARY link metadata)
Applications Image Area
(code & resources)
Applications Runtime Area
(static fields & internal structures)
NOTE:
Content in RAM is Read/Write by MEJ32.
Content in ROM is Read-Only by MEJ32.
Kernel
Core Engine

## Slide 3: Overview (In-PlacE)
Kernel.install(InputStream)
.fo
1
2
Apply code relocations
Feature.start()
Allocate and transfer bytes stream
To Kernel Working Buffer

## Slide 4: MemorIES (IN-PLACE)
Kernel Working Buffer
(Code and Resources)
RAM
ROM
Java Heap
(TEMPORARY link metadata)
Core Engine
NOTE:
Content in RAM is Read/Write by MEJ32.
Content in ROM is Read-Only by MEJ32.
Kernel Code